## Slide 1: COMPUTER ORGANIZATION & ARCHITECTURE

## Slide 2
Unit-4
Central Processing Unit

## Slide 3: Central Processing Unit
1. Introduction
2. General Register Organization
3. Stack Organization
4. Instruction Formats
5. Addressing Modes
6. Data Transfer and Manipulation
7. Program Control
8. Reduced Instruction Set Computer(RISC)

## Slide 4: Central Processing Unit
The Components with in the CPU
  1) Register Sets
  2) Arithmetic and Logical Unit
  3) Control Unit
  Register sets
    Single Accumulator organization (Special purpose reg)
    b) General Register Organization
    c) Stack Organization

## Slide 5: MAJOR COMPONENTS OF CPU
Storage Components
  Registers
  Flags
Execution (Processing) Components
  Arithmetic Logic Unit(ALU)
    Arithmetic calculations, Logical computations, Shifts/Rotates
Transfer Components
  Bus
Control Components
  Control Unit
Register
File
ALU
Control Unit

## Slide 6
In general, most processors are organized in one of 3 ways
  1. Single register (Accumulator) organization
    Basic Computer is a good example
    Accumulator is the only general purpose register
  2. General register organization
    Used by most modern computer processors
    Any of the registers can be used as the source or destination for computer operations
  3. Stack organization
    All operations are done using the hardware stack
    For example, an OR instruction will pop the two top elements from the stack, do a logical OR on them, and push the result on the stack

## Slide 7
In a Single Accumulator Organization there are few special purpose registers
In any CPU the total registers can be divided into different groups
i) General purpose registers ii) Special purpose registers
Special purpose registers
PC – Program Counter
AR – Address Register
IR – Instruction Register
DR – Data Register
AC – Accumulator
TR – Temporary Register
INRR – Input Register
OUPR – Output Register
General Purpose Register
R1
.
.
.
.
.
.
.
Rn

## Slide 8
Bus organization for CPU registers
Control word
A general organization of seven CPU registers
Consider R1 ← R2 + R3, the following are the functions implemented within the CPU
MUX A Selector (SELA) − It can place R2 into bus A.
MUX B Selector (SELB) − It can place R3 into bus B.
ALU Operation Selector (OPR) − It can select the arithmetic addition (ADD).
Decoder Destination Selector (SELD) − It can transfers the result into R1.

## Slide 9
Encoding of Register Selection Fields
Encoding of ALU operations
Control word

## Slide 10: A Stack Machine
10
A Stack machine has a stack as a part of the processor state
typical operations:
    push, pop, +, *, ...
Instructions like + implicitly
specify the top 2 elements of the stack as operands.
a
:
stack
Processor
Main
Store
b
a
push b

c
b
a
push c

b
a
pop

LIFO : Last In First Out
Notes: CS252 S05
10

## Slide 11: REGISTER STACK ORGANIZATION
Register Stack
Push, Pop operations
/* Initially, SP = 0, EMPTY = 1, FULL = 0 */
PUSH
POP
  SP  SP + 1 DR  M[SP]
  M[SP]  DR SP  SP  1
  If (SP = 0) then (FULL  1) If (SP = 0) then (EMPTY  1)
  EMPTY  0 FULL  0
Stack
- Very useful feature for nested subroutines, nested interrupt services
- Also efficient for arithmetic expression evaluation
- Storage which can be accessed in LIFO
- Pointer: SP (stack Pointer)
- Only PUSH and POP operations are applicable
A
B
C
0
1
2
3
4
63
Address
FULL
EMPTY
SP
DR
Flags
Stack pointer
stack
6 bits
A register stack is a memory space that uses memory words or registers to store temporary information during program execution.
64 Word Stack

## Slide 12: MEMORY STACK ORGANIZATION
- PUSH: SP  SP - 1
  M[SP]  DR
Memory with Program, Data, and Stack Segments
4001
4000
3999
3998
3997
3000
Data
(operands)
Program
(instructions)
1000
PC
AR
SP
stack
Stack grows
In this direction
RAM
A portion of memory is assigned to a stack operation to implement the stack in the CPU.
Program Counter (PC): It is a register that points to the address of the next instruction that is going to be executed in the program.
Address Register (AR): This register points at the collection of data and is used during the execute phase to read an operand.
Stack Pointer (SP): It points at the top of the stack and is used to push or pop the data items in or from the stack.
- POP: DR  M[SP]
  SP  SP + 1
- A portion of memory is used as a stack with a processor register as
a stack pointer

## Slide 13
In-fix expression (X + Y)
Pre-fix or polish notation ( +XY )
Post fix expression or reverse polish notation (XY +)

## Slide 14: Evaluation of Expressions
a
b
c
(a + b * c) / (a + d * c - e)
/
+
*
+
a
e
-
a
c
d
c
*
b
Reverse Polish
a b c * + a d c * + e - /
push a
push b
push c
multiply
*
Evaluation Stack
b * c
Notes: CS252 S05
14

## Slide 15: REVERSE POLISH NOTATION
A + B Infix notation
+ A B Prefix or Polish notation
A B + Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free
Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Arithmetic Expressions: A + B
3
3
12
12
12
12
42
4
5
5
6
30
3
4
*
5
6
*
+

## Slide 16: INSTRUCTION FORMAT
OP-code field - specifies the operation to be performed
Address field - designates memory address(es) or a processor register(s)
Mode field - determines how the address field is to be interpreted (to
get effective address or the operand)
The number of address fields in the instruction format
depends on the internal organization of CPU
The three most common CPU organizations:
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */ CLA – Clear the accumulator; CMA
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD
Instruction Fields

## Slide 17: THREE, AND TWO-ADDRESS INSTRUCTIONS
Three-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[A] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */

## Slide 18: ONE, AND ZERO-ADDRESS INSTRUCTIONS
One-Address Instructions
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */
Zero-Address Instructions
- Can be found in a stack-organized computer
- Program to evaluate X = (A + B) * (C + D) :
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */

## Slide 19
X = (A + B) * (C + D) | 
Three Instruction format ADD R1, A, B R1  M[A] + M[B] ADD R2, C, D R2  M[C] + M[D] MUL X, R1, R M[X]  R1 * R2 | Two Instruction format MOV R1, A R1  M[A] ADD R1, B R1  R1 + M[B] MOV R2, C R2  M[C] ADD R2, D R2  R2 + M[D] MUL R1, R2 R1  R1 * R2 MOV X, R1 M[X]  R1
Single Instruction format LOAD A AC  M[A] ADD B AC  AC + M[B] STORE T M[T]  AC LOAD C AC  M[C] ADD D AC  AC + M[D] MUL T AC  AC * M[T] STORE X M[X]  AC | Zero Instruction format PUSH A TOS  A PUSH B TOS  B ADD TOS  (A + B) PUSH C TOS  C PUSH D TOS  D ADD TOS  (C + D) MUL TOS  (C + D) * (A + B) POP X M[X]  TOS

## Slide 20
X = (A + B) * (C + D)
Reduced instruction set Computer (RISC) MOV R1, A R1  M[A] MOV R2, B R2  M[B] MOV R3, C R3  M[C] MOV R4, A R4  M[D] ADD R1, R2 R1  R1 + R2 ADD R3, R4 R3  R3 + R4 MUL R1, R3 R1  R1 * R3 STORE X, R1 M[X]  R1

## Slide 21
Types of Addressing Modes
Implied
Immediate
Direct
Indirect
Register
Register Indirect
Autoincrement or AutoDecrement
Relative
Indexed
Base Register

## Slide 22
An assembly language program instruction consists of two parts

## Slide 23: Implied Addressing Mode
Implied Mode
Address of the operands are specified implicitly in the definition of the instruction
- No need to specify address in the instruction
- EA = AC, or EA = Stack[SP]
- Examples from Basic Computer
CLA, CME, INP
Zero address instruction are designed with implied addressing mode.

## Slide 24: Immediate Addressing
Immediate Mode
Instead of specifying the address of the operand,
operand itself is specified
- No need to specify address in the instruction
- However, operand itself needs to be specified
- Sometimes, require more bits than the address
- Fast to acquire an operand
e.g. ADD 5
  Add 5 to contents of accumulator
  5 is operand
Example: MOV AL, 35H (move the data 35H into AL register)
Opcode
Operand
Instruction

## Slide 25
Direct Addressing
Direct Address Mode
Instruction specifies the memory address which can be used directly to access the memory
- Faster than the other memory addressing modes
- Too many bits are needed to specify the address
for a large physical memory space
- EA = IR(addr) (IR(addr): address field of IR)
e.g. ADD A
  Add contents of cell A to accumulator
  Look in memory at address A for operand

## Slide 26
Direct Addressing Diagram
Address A
Opcode
Instruction
Memory
Operand
Example: ADD AL,[0301] //add the contents of offset address 0301 to AL

## Slide 27
Indirect Addressing
Indirect Addressing Mode
The address field of an instruction specifies the address of a memory location that contains the address of the operand
- When the abbreviated address is used large physical memory can be addressed with a relatively small number of bits
- Slow to acquire an operand because of an additional memory access
- EA = M[IR(address)]
EA = (A)
  Look in A, find address (A) and look there for operand
e.g. ADD (A)
  Add contents of cell pointed to by contents of A to accumulator

## Slide 28
Indirect Addressing Diagram
Address A
Opcode
Instruction
Memory
Operand
Pointer to operand

## Slide 29
Register Addressing
Register Mode
Address specified in the instruction is the register address
- Designated operand need to be in a register
- Shorter address than the memory address
- Saving address field in the instruction
- Faster to acquire an operand than the memory addressing
- EA = IR(R) (IR(R): Register field of IR)
EA = R

## Slide 30
Register Addressing Diagram
Register Address R
Opcode
Instruction
Registers
Operand

## Slide 31
Register Indirect Addressing
Register Indirect Mode
Instruction specifies a register which contains the memory address of the operand
- Saving instruction bits since register address
is shorter than the memory address
- Slower to acquire an operand than both the
register addressing or memory addressing
- EA = [IR(R)] ([x]: Content of x)
EA = (R)

## Slide 32
Register Indirect Addressing Diagram
Register Address R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers

## Slide 33
Index Addressing Diagram
Register R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers
Address A
+

## Slide 34: DATA TRANSFER INSTRUCTIONS
Typical Data Transfer Instructions
Load LD
Store ST
Move MOV
Exchange XCH
Input IN
Output OUT
Push PUSH
Pop POP
Name Mnemonic
Direct address LD ADR AC M[ADR]
Indirect address LD @ADR AC  M[M[ADR]]
Relative address LD $ADR AC  M[PC + ADR]
Immediate operand LD #NBR AC  NBR
Index addressing LD ADR(X) AC  M[ADR + XR]
Register LD R1 AC  R1
Register indirect LD (R1) AC  M[R1]
Autoincrement LD (R1)+ AC  M[R1], R1  R1 + 1
Autodecrement LD -(R1) R1  R1 - 1, AC  M[R1]
Mode
Assembly
Convention
Register Transfer
Data Transfer Instructions with Different Addressing Modes

## Slide 35: DATA MANIPULATION INSTRUCTIONS
Three Basic Types:
Arithmetic instructions
Logical and bit manipulation instructions
Shift instructions
Arithmetic Instructions
Name Mnemonic
Logical and Bit Manipulation Instructions
Clear CLR
Complement COM
AND AND
OR OR
Exclusive-OR XOR
Clear carry CLRC
Set carry SETC
Complement carry COMC
Enable interrupt EI
Disable interrupt DI
Name Mnemonic
Logical shift right SHR
Logical shift left SHL
Arithmetic shift right SHRA
Arithmetic shift left SHLA
Rotate right ROR
Rotate left ROL
Rotate right thru carry RORC
Rotate left thru carry ROLC
Name Mnemonic
Shift Instructions
Increment INC
Decrement DEC
Add ADD
Subtract SUB
Multiply MUL
Divide DIV
Add with Carry ADDC
Subtract with Borrow SUBB
Negate(2’s Complement) NEG

## Slide 36
Control memory

## Slide 37
Address Sequencing

## Slide 38
Micro Programme Example

## Slide 40
Design of Control Unit