## Slide 1: Unit 2
PROJECTION OF POINTS AND PROJECTION OF LINES

## Slide 2
PROJECTION OF POINTS

## Slide 3: Introduction
A point is defined as a geometrical element that has no dimension. In engineering drawing, a point is represented by a dot.
Quadrant system: The picture planes used for obtaining the orthographic projections are called the Principal planes of projection or reference planes or co- ordinate planes of projection.
VP: The plane in front of observer is the vertical plane. (VP) or it is also called a Frontal plane. Front View (FV): The projection on the VP is called the Front View (FV) or Vertical Projection or front elevation or Elevation.
HP: The plane which is Horizontal and perpendicular to VP is Horizontal Plane.
Top View (TV): The projection on the HP is called the Top View (TV) or Horizontal Projection or Plan.
Note: The planes HP and VP are called Principal Planes.
Reference Line: The line of intersection of HP and VP is called reference line, which is denoted by X-Y.

## Slide 6: QUADRANTS

## Slide 7: QUADRANTS

## Slide 8: QUADRANTS

## Slide 9: QUADRANTS

## Slide 10: FIRST QUADRANT

## Slide 11: FIRST QUADRANT

## Slide 12: FIRST QUADRANT

## Slide 13: FIRST QUADRANT

## Slide 14: FIRST QUADRANT

## Slide 15: SECOND QUADRANT

## Slide 16: THIRD QUADRANT

## Slide 17: FOURTH QUADRANT

## Slide 18: POSITION OF POINTS IN VARIOUS QUADRANTS
Denoted as a’, b’ etc.
Denoted as a, b etc.

## Slide 19: POSITION OF POINTS IN VARIOUS QUADRANTS

## Slide 20
1. 70 mm above HP and 50mm in front of VP
2. 50 mm below HP and 60mm behind VP

## Slide 21
3. 70mm above HP and 40mm behind the VP
4. 70mm below the HP and 35 mm infront of VP.

## Slide 22
5. On HP and 40mm infront of VP
6. On HP and 40 mm behind the VP

## Slide 23
7. Point on VP and 70mm above HP
8. Point on VP and 65mm below HP
9. Point on both HP and VP

## Slide 24
10. Draw the projections of the following points on a common reference line keeping the distance between their projectors 40mm apart.
Point A is 50mm above the H.P and 40mm in front of the V.P.
Point B is 60mm above the H.P and 30mm behind the VP.
Point C is 30mm below the HP and 40mm behind the VP.
Point D is 50mm below the HP. and 40mm in front of the VP.
Point D is 50mm in front of the VP and in the HP.

## Slide 25
11. Draw the projections of the following points on the same ground line, keeping the projectors 25 mm apart.
i. A is in the H.P. and 20 mm behind the V.P.
ii. B is 40 mm above the H.P. and 25 mm in front of the V.P.
iii. C is in the V.P. and 40 mm above the H.P.
iv. D is 25 mm below the H.P. and 25 mm behind the V.P.
v. E is 15 mm above the H.P. and 50 mm behind the V.P.
vi. F is 40 mm below the H.P. and 25 mm in front of the V.P.
vii. G is in both the H.P. and the V.P.

## Slide 26
12. Draw the orthographic projections of the following points.
i. Point P is30 mm . above H.P and 40mm in front of VP.
ii. Point Q is25 mm. Above H.P and 35mm behind VP.
iii. Point R is 32 mm. below H.P and 45mm behind VP.
iv. Point S is 35 mm. below H.P and 42mm in front to VP.
v. Point T is in H.P and 30 mm behind VP.
vi. Point U is in V.P and 40 mm. below HP.
vii. Point V is in V.P and 35 mm. above H.P.
viii. Point W is in H.P and 48 mm. in front of VP.

## Slide 27
13. Draw the projections of the following points on the same XY line, keeping convenient distance between each projectors. Name the quadrants in which they lie.
i. Point A is 30 mm above HP and 35 mm in front of VP.
ii. Point B is 35 mm above HP and 40 mm behind VP.
iii. Point C is 40 mm above HP and on VP.
iv. Point D is 35 mm below HP and 30 mm in front of VP.

## Slide 28
14. Draw the projections of the following points on the same XY line, keeping convenient distance between each projectors. Name the Quadrants in which they lie.
i. Point E is 30 mm below HP and 25 mm behind VP.
ii. Point F is 35 mm below HP and 30 mm in front of VP.
iii. Point G is on HP and 30 mm in front of VP.
iv. Point H is on HP and 35 mm behind VP.