## Slide 1: COMPUTER ORGANIZATION & ARCHITECTURE

## Slide 2
Unit-3
Basic Computer Organization & Design

## Slide 3: Basic Computer Organization & Design
1. Instruction Codes
2. Computer Registers
3. Computer Instructions
4. Timing and Control
5. Instruction Cycle
6. Memory-Reference Instructions
7. Input-Output and Interrupt
8. Complete Computer Description
9. Design of Basic Computer
10. Design of Accumulator Logic

## Slide 4
Instruction Codes
Instruction Codes:
* The organization of the computer is defined by its internal registers, the timing and control structure, and the set of instructions that it uses.
* Internal organization of a computer is defined by the sequence of micro-operations it performs on data stored in its registers.
Computer can be instructed about the specific sequence of operations it must perform.
User controls this process by means of a Program.
* Program: set of instructions that specify the operations, operands, and the sequence by which processing has to occur.
* Instruction: a binary code that specifies a sequence of micro-operations for the computer.

## Slide 5
The computer reads each instruction from memory and places it in a control register. The control then interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro-operations. – Instruction Cycle
Instruction Code: group of bits that instruct the computer to perform specific operation.
Instruction code is usually divided into two parts: Opcode and address(operand)

## Slide 6
Instruction Codes
Instruction Format
The Operation code (Opcode) field determines the process that needs to be performed
The Mode field specifies
how the operand locates
The Address field contains the operand's location, i.e., register or memory location.
11
0
12
14
15

## Slide 7
Operation Code (opcode):
Group of bits that define the operation
Eg: add, subtract, multiply, shift, complement.
No. of bits required for opcode depends on no. of operations available in computer.
n bit opcode >= 2 n (or less) operations
Address (operand):
Specifies the location of operands (registers or memory words)
Memory words are specified by their address
Registers are specified by their k-bit binary code
k-bit address >= 2 k registers

## Slide 8
Stored Program Organization:
The ability to store and execute instructions is the most important property of a general-purpose computer. That type of stored program concept is called stored program organization.
The simplest way to organize a computer is to have one processor register and an instruction code format with two parts. The first part specifies the operation to be performed and the second specifies an address.

## Slide 9
* Instructions are stored in one section of memory and data in another.
For a memory unit with 4096 words we need 12 bits to specify an address since 212 = 4096.
If we store each instruction code in one 16-bit memory word, we have available four bits for the operation code (abbreviated opcode) to specify one out of 16 possible operations, and 12 bits to specify the address of an operand.
Accumulator (AC):
Computers that have a single-processor register usually assign to it the name accumulator and label it AC.
The operation is performed with the memory operand and the content of AC.

## Slide 10
Addressing of Operand:
Addressing of Operand

## Slide 11
Computer Registers
Computer Registers:
What is the need for computer registers?
The need of the registers in computer for Instruction sequencing needs a counter to calculate the address of the next instruction after execution of the current instruction is completed (PC).
Necessary to provide a register in the control unit for storing the instruction code after it is read from memory (IR).
Needs processor registers for manipulating data (AC and TR) and a register for holding a memory address (AR).

## Slide 13: COMMON BUS SYSTEM
S2
S1
Bus
S0
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register
Common Bus System

## Slide 14
Instructions are of three types
Register reference instructions
Memory reference instructions
IO reference instruction
12 bits to specify an address
Addressing mode
I = 0 : direct addressing
I = 1 : indirect addressing

## Slide 16
Timing and Control
Timing and Control
The timing for all registers in the basic computer is controlled by a master clock generator.
The clock pulses are applied to all flip-flops and registers in the system, including the flip-flops and registers in the control unit.
The clock pulses do not change the state of a register unless the register is enabled by a control signal.
The control signals are generated in the control unit and provide control inputs for the multiplexers in the common bus, control inputs in processor registers, and micro operations for the accumulator.
There are two major types of control organization: o Hardwired control o Micro programmed control

## Slide 21
Instruction Cycle
Instruction Cycle
Every program is a collection of instructions
Each instruction of the program is executed using instruction cycle.
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory (Retrieving Instruction from the memory)
  Decode the instruction (which operation the corresponding instruction will perform)
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
START
HALT
Fetch Next
Instruction
Execute
Instruction

## Slide 23
Fetch and Decode
Initially, the program counter PC is loaded with the address of the first instruction in the program
The sequence counter SC is cleared to 0, providing a decoded timing signal T0
The micro operations for the fetch and decode phases can be specified by the following register transfer statements

## Slide 25
MEMORY REFERENCE INSTRUCTIONS
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
The effective address of the instruction is in AR and was placed there during timing signal T2 when I = 0, or
during timing signal T3 when I = 1
Memory cycle is assumed to be short enough to complete in a CPU cycle
The execution of MR instruction starts with T4
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 26
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address
M[AR]  PC, PC  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T4: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 27
FLOWCHART FOR MEMORY REFERENCE INSTRUCTIONS
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 28
Input-Output and Interrupt
Input-Output and Interrupt
Instructions and data stored in memory must come from some input device.
Computational results must be transmitted to the user through some output device
To demonstrate the most basic requirements for input and output communication, we will use as an illustration a terminal unit with a keyboard and printer

## Slide 29
Input-Output Configuration

## Slide 30
Input-Output Instructions

## Slide 31
FLOWCHART FOR INTERRUPT CYCLE
Store return address
R
=1
=0
in location 0
M[0]  PC
Branch to location 1
PC  1
IEN  0
R  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
IEN
FGI
FGO
Execute
instructions
R  1
=1
=1
=1
=0
=0
=0
R = Interrupt flip-flop

## Slide 32
Interrupt cycle
Interrupt cycle
After interrupt cycle
0
BUN
1120
0
1
PC = 256
255
1
BUN
0
Before interrupt
Main
Program
1120
I/O
Program
0
BUN
1120
0
PC = 1
256
255
1
BUN
0
Memory
Main
Program
1120
I/O
Program
256
Register Transfer Statements for Interrupt Cycle
R F/F  1 if IEN (FGI + FGO)T0T1T2
 T0T1T2 (IEN)(FGI + FGO): R  1
The fetch and decode phases of the instruction cycle
must be modified  Replace T0, T1, T2 with R'T0, R'T1, R’T2
The interrupt cycle :
RT0: AR  0, TR  PC
RT1: M[AR]  TR, PC  0
RT2: PC  PC + 1, IEN  0, R  0, SC  0

## Slide 33
COMPLETE COMPUTER DESCRIPTION Flowchart of Operations
=1 (I/O) =0 (Register) =1(Indir) =0(Dir)
start
SC  0, IEN  0, R  0
R
AR  PC
R’T0
IR  M[AR], PC  PC + 1
R’T1
AR  IR(0~11), I  IR(15)
D0...D7  Decode IR(12 ~ 14)
R’T2
AR  0, TR  PC
RT0
M[AR]  TR, PC  0
RT1
PC  PC + 1, IEN  0
R  0, SC  0
RT2
D7
I
I
Execute
I/O
Instruction
Execute
RR
Instruction
AR <- M[AR]
Idle
D7IT3 D7I’T3
D7’IT3 D7’I’T3
Execute MR
Instruction
=0(Instruction Cycle) =1(Interrupt Cycle)
=1(Register or I/O) =0(Memory Ref)
D7’T4

## Slide 34
DESIGN OF BASIC COMPUTER(BC)
Hardware Components of BC
A memory unit : 4096 x 16.
Registers: Flip-Flops(Status):
AR, PC, (12 bit) I, S, E, R, IEN, FGI, and FGO
DR, AC, IR, TR, (16 bit)
OUTR, INPR, (8 bit) and
SC (4 bit)
Decoders: 1) 3x8 Opcode decoder 2) 4x16 timing decoder
Common bus: 16 bits
Control logic gates: Adder and Logic circuit: Connected to AC
  Input Controls of the nine registers
  Read and Write Controls of memory
  Set, Clear, or Complement Controls of the flip-flops
  S2, S1, S0 Controls to select a register for the bus
  AC, and Adder and Logic circuit

## Slide 35
COMPLETE COMPUTER DESCRIPTION Microoperations
Fetch
Decode
Indirect
Interrupt
Memory-Reference
AND
ADD
LDA
STA
BUN
BSA
ISZ
RT0:
RT1:
RT2:
D7IT3:
RT0:
RT1:
RT2:
D0T4:
D0T5:
D1T4:
D1T5:
D2T4:
D2T5:
D3T4:
D4T4:
D5T4:
D5T5:
D6T4:
D6T5:
D6T6:
AR  PC
IR  M[AR], PC  PC + 1
D0, ..., D7  Decode IR(12 ~ 14),
AR  IR(0 ~ 11), I  IR(15)
AR  M[AR]
R  1
AR  0, TR  PC
M[AR]  TR, PC  0
PC  PC + 1, IEN  0, R  0, SC  0
DR  M[AR]
AC  AC  DR, SC  0
DR  M[AR]
AC  AC + DR, E  Cout, SC  0
DR  M[AR]
AC  DR, SC  0
M[AR]  AC, SC  0
PC  AR, SC  0
M[AR]  PC, AR  AR + 1
PC  AR, SC  0
DR  M[AR]
DR  DR + 1
M[AR]  DR, if(DR=0) then (PC  PC + 1),
SC  0
T0T1T2(IEN)(FGI + FGO):

## Slide 36
Register-Reference
CLA
CLE
CMA
CME
CIR
CIL
INC
SPA
SNA
SZA
SZE
HLT
Input-Output
INP
OUT
SKI
SKO
ION
IOF
D7IT3 = r
IR(i) = Bi
r:
rB11:
rB10:
rB9:
rB8:
rB7:
rB6:
rB5:
rB4:
rB3:
rB2:
rB1:
rB0:
D7IT3 = p
IR(i) = Bi
p:
pB11:
pB10:
pB9:
pB8:
pB7:
pB6:
(Common to all register-reference instr)
(i = 0,1,2, ..., 11)
SC  0
AC  0
E  0
AC  AC
E  E
AC  shr AC, AC(15)  E, E  AC(0)
AC  shl AC, AC(0)  E, E  AC(15)
AC  AC + 1
If(AC(15) =0) then (PC  PC + 1)
If(AC(15) =1) then (PC  PC + 1)
If(AC = 0) then (PC  PC + 1)
If(E=0) then (PC  PC + 1)
S  0
(Common to all input-output instructions)
(i = 6,7,8,9,10,11)
SC  0
AC(0-7)  INPR, FGI  0
OUTR  AC(0-7), FGO  0
If(FGI=1) then (PC  PC + 1)
If(FGO=1) then (PC  PC + 1)
IEN  1
IEN  0

## Slide 37
LD(AR) = R'T0 + R'T2 + D'7IT3
CLR(AR) = RT0
INR(AR) = D5T4
Scan all of the register transfer statements that change the content of AR:
Address Register; AR
R’T0: AR  PC LD(AR)
R’T2: AR  IR(0-11) LD(AR)
D’7IT3: AR  M[AR] LD(AR)
RT0: AR  0 CLR(AR)
D5T4: AR  AR + 1 INR(AR)
AR
LD
INR
CLR
Clock
To bus
12
From bus
12
D'
I
T
T
R
T
D
T
7
3
2
0
4
CONTROL OF REGISTERS AND MEMORY

## Slide 38
CONTROL OF FLAGS
pB7: IEN <- 1 (I/O Instruction)
pB6: IEN <- 0 (I/O Instruction)
RT2: IEN <- 0 (Interrupt)
p = D7IT3 (Input/Output Instruction)
IEN: Interrupt Enable Flag
D
I
T3
7
J
K
Q
IEN
p
B
7
B
6
T
2
R

## Slide 39
CONTROL OF COMMON BUS
For AR
D4T4: PC <- AR
D5T5: PC <- AR
x1 = D4T4 + D5T5
x1
x2
x3
x4
x5
x6
x7
Encoder
S
2
S
1
S
0
Multiplexer
bus select
inputs
x1 x2 x3 x4 x5 x6 x7
S2 S1 S0
selected
register
0 0 0 0 0 0 0 0 0 0 none
1 0 0 0 0 0 0 0 0 1 AR
0 1 0 0 0 0 0 0 1 0 PC
0 0 1 0 0 0 0 0 1 1 DR
0 0 0 1 0 0 0 1 0 0 AC
0 0 0 0 1 0 0 1 0 1 IR
0 0 0 0 0 1 0 1 1 0 TR
0 0 0 0 0 0 1 1 1 1 Memory

## Slide 40
DESIGN OF ACCUMULATOR LOGIC
Circuits associated with AC
All the statements that change the content of AC
16
16
8
Adder and
logic
circuit
16
AC
From DR
From INPR
Control
gates
LD
INR
CLR
16
To bus
Clock
D0T5: AC <- AC  DR AND with DR
D1T5: AC <- AC + DR Add with DR
D2T5: AC <- DR Transfer from DR
pB11: AC(0-7) <- INPR Transfer from INPR
rB9: AC <- AC Complement
rB7 : AC <- shr AC, AC(15) <- E Shift right
rB6 : AC <- shl AC, AC(0) <- E Shift left
rB11 : AC <- 0 Clear
rB5 : AC <- AC + 1 Increment