## Slide 1: COMPUTER ORGANIZATION & ARCHITECTURE

## Slide 2: COURSE STRUCTURE (MR22-1CS0142)
UNIT-1
Digital Components: Integrated Circuits, Decoders, Multiplexers, Registers, Shift Registers, Binary Counters, Memory Unit.
Data Representation: Data Types, Complements, Fixed-Point Representation, Conversion of Fractions, Floating-Point Representation, Other Binary Codes, Error Detection Codes.
UNIT-2
Register Transfer and Microoperations: Register Transfer Language, Register Transfer, Bus and Memory Transfers, Arithmetic Microoperations, Logic Microoperations, Shift Microoperations, Arithmetic Logic Shift Unit.
UNIT-3
Basic Computer Organization and Design: Instruction Codes, Computer Registers, Computer Instructions, Timing and Control, Instruction Cycle, Memory-Reference Instructions, Input-Output and Interrupt, Complete Computer Description, Design of Basic Computer, Design of Accumulator Logic.

## Slide 3: COURSE STRUCTURE (MR22-1CS0142)
UNIT-4
Central Processing Unit: Introduction, General Register Organization, Stack Organization, Instruction Formats, Addressing Modes, Data Transfer and Manipulation, Program Control, Reduced Instruction Set Computer(RISC)
UNIT-5
Input-Output Organization: Peripheral Devices, Input-Output Interface, Asynchronous Data Transfer, Modes of Transfer, Priority Interrupt, Direct Memory Access (DMA), Input- Output Processor (IOP), Serial Communication, Bus Standards.

## Slide 4: Digital Components
Unit-1
Data Representation

## Slide 5: Digital Components
» Integrated Circuits
» Decoders
» Multiplexers
» Registers
» Shift Registers
» Binary Counters
» Memory Unit

## Slide 6
Integrated Circuits
Digital circuits are constructed with integrated circuits. An integrated circuit (abbreviated IC) is a small silicon semiconductor crystal called a chip, containing the electronic components for the digital gates.
The various gates are interconnected inside the chip to form the required circuit
The chip is mounted in a ceramic or plastic container, and connections are welded by thin gold wires to external pins to form the integrated circuit.
The number of pins may range from 14 in a small IC package to 100 or more in a larger package. Each IC has a numeric designation printed on the surface of the package for identification.

## Slide 7
Integrated Circuits
Small-scale integration (SSI): devices contain several independent gates in a single package. The inputs and outputs of the gates are connected directly to the pins in the package. The number of gates is usually less than 10 and is limited by the number of pins available in the IC.
Medium-scale integration (MSI): devices have a complexity of approximately 10 to 200 gates in a single package. They usually perform specific elementary digital functions such as decoders, adders, and registers.
Large-scale integration (LSI): devices contain between 200 and a few thousand gates in a single package. They include digital systems, such as processors, memory chips, and programmable modules.
Very-large-scale integration (VLSI): devices contain thousands of gates within a single package. Examples are large memory arrays and complex microcomputer chips.
Super large scale integration (SLSI): devices contain between 10,000 and 1,00,000 gates within a single package and perform computational operations such as microprocessor chips, micro-controllers, basic PICs (Peripheral Interface Controller) and calculator.
Scale of Integration or Classification of integrated circuits

## Slide 8
Integrated Circuits
Ultra large scale integration (ULSI): devices contain More than 1 million gates and it is used in computers CPUs, GPUs, Video processors.
Logic Families:
The IC technology usually depends on the following factors:
          1) Speed.
          2) Power description.
          3) Noise immunity.
          4) Input/output interface compatibility.
          5) Cost.
Digital Integrated Circuits:
The advantages if ICs being used in digital systems are
1) Small size.
2) High reliability.
3) Low cost.
4) Low power consumption.

## Slide 9
Integrated Circuits
There are two broad categories of digital ICs. They are
Fixed function logic
Programmable logic
Fixed function logic: The logic function of IC are set by the manufacturer and cannot be altered.
Programmable logic: The logic function of IC can be altered.
The two basic techniques for manufacturing ICs are
Bipolar techniques
Metal Oxide Semiconductor (MOS) techniques

## Slide 10
Integrated Circuits
Classification of digital ICs families are
1. Bipolar techniques
      > Resistor transistor logic (RTL)
      > Diode transistor logic (DTL)
      > Transistor transistor logic (TTL)
      > Emitter coupled logic (ECL)
2. Metal Oxide Semiconductor techniques
> P channel MOSFET (PMOS)
> N channel MOSFET (NMOS)
> Complementary MOSFET (CMOS)

## Slide 11
Block Diagram of a Digital Computer
Basics

## Slide 12
Basics

## Slide 13
Digital Logic Gates
X | Y
0 | 0
0 | 1
1 | 0
1 | 1
Basics

## Slide 14
Example-1
Basics
Consider an example Boolean equation representing electrical or electronic logic for control of the lowering of the driver’s power window in a car.
Truth Table Logic Circuit Diagram
Truth Table

## Slide 15
Basic Identities of Boolean Algebra
Basics

## Slide 16
Primitive Digital Logic Gates
AND
OR
NOT
NAND
NOR
BUFFER

## Slide 17
DECODERS
A decoder is a combinational circuit that converts binary information from the n coded inputs to a maximum of 2 unique outputs.
A decoder has n inputs and m outputs and is also referred to as an n x m decoder
n x 2n
If n = 2 ; 2 x 4 decoder or 2 to 4 line decoder
If n = 3 ; 3 x 8 decoder or 3 to 8 line decoder
If n = 4 ; 4 x 16 decoder or 4 to 16 line decoder
If n = 5 ; 5 x 32 decoder or 5 to 32 line decoder
n input lines
2n Output lines

## Slide 18
DECODERS
Y3 = E.A1.A0 Y2 = E.A1.A0’ Y1 = E.A1’.A0 Y0 = E.A1'.A0'
TRUTH TABLE
2 to 4 line decoder
Block Diagram
Logical expression

## Slide 19
DECODERS
Logical circuit

## Slide 20
DECODERS
Y0=A0'.A1'.A2’ Y1=A0.A1'.A2' Y2=A0'.A1.A2’ Y3=A0.A1.A2’
Y4=A0'.A1’.A2 Y5=A0.A1'.A2 Y6=A0'.A1.A2 Y7=A0.A1.A2
3 to 8 line decoder
Truth Table
Block Diagram
Logical expression

## Slide 21
DECODERS
Logical circuit

## Slide 22
DECODERS
4 to 16 line decoder using two 3 to 8 line decoder
Block Diagram

## Slide 23
DECODERS
Y0=A0'.A1'.A2'.A3' Y1=A0'.A1'.A2'.A3 Y2=A0'.A1'.A2.A3' Y3=A0'.A1'.A2.A3 Y4=A0'.A1.A2'.A3' Y5=A0'.A1.A2'.A3 Y6=A0'.A1.A2.A3' Y7=A0'.A1.A2.A3 Y8=A0.A1'.A2'.A3' Y9=A0.A1'.A2'.A3 Y10=A0.A1'.A2.A3' Y11=A0.A1'.A2.A3 Y12=A0.A1.A2'.A3' Y13=A0.A1.A2'.A3 Y14=A0.A1.A2.A3' Y15=A0.A1.A2'.A3
Truth Table
Logical expression

## Slide 24
DECODERS
Logical circuit

## Slide 25
Encoders
Encoder performs the reverse operation of the Decoder
If n = 2 ; 4 x 2 encoder or 4 to 2 line encoder
If n = 3 ; 8 x 3 encoder or 8 to 3 line encoder
If n = 4 ; 16 x 4 encoder or 16 to 4 line encoder
If n = 5 ; 32 x 5 encoder or 32 to 5 line encoder
n x 2n
n output lines
2n input lines

## Slide 26
4 to 2 line Encoder
Encoders
Block Diagram

## Slide 27
A1=Y3+Y2
A0=Y3+Y1
Encoders
Truth Table
Logical expression

## Slide 28
Encoders
Logical circuit

## Slide 29
8 to 3 line Encoder
Encoders
Block Diagram

## Slide 30
A2=Y4+Y5+Y6+Y7
A1=Y2+Y3+Y6+Y7
A0=Y7+Y5+Y3+Y1
Encoders
Truth Table
Logical expression

## Slide 31
Encoders
Logical circuit

## Slide 32
Multiplexers
A multiplexer is a combinational circuit that has 2n input lines and a single output line.
A De-multiplexer is a combinational circuit that has only 1 input line and 2N output lines.
2×1 Multiplexer
4×1 Multiplexer
8×1 Multiplexer
16×1 Multiplexer
Multiplexer
1×2 De-multiplexer
1×4 De-multiplexer
1×8 De-multiplexer
1×16 De-multiplexer
De-Multiplexer

## Slide 33
Multiplexers
2×1 Multiplexer
Truth Table
Y= S0'.A0+S0.A1
Logical circuit
Block Diagram
Logical expression

## Slide 34
Multiplexers
4×1 Multiplexer
Y=S1' S0' A0+S1' S0 A1+S1 S0' A2+S1 S0 A3
Truth Table
Block Diagram
Logical expression

## Slide 35
Multiplexers
Logical circuit

## Slide 36
Multiplexers
8 to 1 Multiplexer
Truth Table
Block Diagram

## Slide 37
Multiplexers
Y=S0'.S1'.S2’.A0 + S0.S1'.S2'.A1+
S0'.S1.S2’.A2 + S0.S1.S2'.A3+
S0'.S1'.S2 A4 + S0.S1'.S2 A5+
S0'.S1.S2 .A6 + S0.S1.S3.A7
Logical circuit
Logical expression

## Slide 38
Multiplexers
8 ×1 multiplexer using 4×1 and 2×1 multiplexer
Block Diagram

## Slide 39
Multiplexers
16 to 1 Multiplexer
Y=A0.S0'.S1'.S2'.S3’+
A1.S0'.S1'.S2 '.S3+
A2.S0'.S1'.S2.S3’+
A3.S0'.S1 '.S2.S3+
A4.S0'.S1.S2'.S3’+
A5.S0 '.S1.S2'.S3+
A6.S1.S2.S3’+
A7.S0 '.S1.S2.S3+
A8.S0.S1'.S2'.S3’+
A9 .S0.S1'.S2'.S3+
A10.S0.S1'.S2.S3 ’+
A11.S0.S1'.S2.S3+
A12 S0.S1.S2 '.S3’+
A13.S0.S1.S2'.S3+
A14.S0.S1 .S2.S3’+
A15.S0.S1.S2'.S3

## Slide 40
Multiplexers
Logical circuit

## Slide 41
Multiplexers
16×1 multiplexer using 8×1 and 2×1 multiplexer
Block Diagram

## Slide 42
De-Multiplexers
1×2 De-multiplexer
A De-multiplexer is a combinational circuit that has only 1 input line and 2N output lines. Simply, the multiplexer is a single-input and multi-output combinational circuit.
Truth Table
Y0=S0’.A
Y1=S0.A
Logical circuit
Block Diagram
Logical expression

## Slide 43
De-Multiplexers
1×4 De-multiplexer
Y0=S1' S0' A y1=S1' S0 A y2=S1 S0' A y3=S1 S0 A
Truth Table
Block Diagram
Logical expression

## Slide 44
De-Multiplexers
Logical circuit

## Slide 45
De-Multiplexers
1×8 De-multiplexer
Y0=S0'.S1'.S2'.A Y1=S0.S1'.S2'.A
Y2=S0'.S1.S2'.A Y3=S0.S1.S2'.A
Y4=S0'.S1'.S2 A Y5=S0.S1'.S2 A
Y6=S0'.S1.S2 A Y7=S0.S1.S3.A
Truth Table
Block Diagram
Logical expression

## Slide 46
De-Multiplexers
Y0=S0'.S1'.S2'.A
Y1=S0.S1'.S2'.A
Y2=S0'.S1.S2'.A
Y3=S0.S1.S2'.A
Y4=S0'.S1'.S2 A
Y5=S0.S1'.S2 A
Y6=S0'.S1.S2 A
Y7=S0.S1.S3.A
Logical circuit
Logical expression

## Slide 47
De-Multiplexers
1×8 De-multiplexer using 1×4 and 1×2 de-multiplexer
Block Diagram

## Slide 48
De-Multiplexers
1 x 16 De-multiplexer
Block Diagram

## Slide 49
De-Multiplexers
Truth Table
Y0=A.S0'.S1'.S2'.S3' Y1=A.S0'.S1'.S2'.S3 Y2=A.S0'.S1'.S2.S3' Y3=A.S0'.S1'.S2.S3 Y4=A.S0'.S1.S2'.S3' Y5=A.S0'.S1.S2'.S3 Y6=A.S0'.S1.S2.S3' Y7=A.S0'.S1.S2.S3 Y8=A.S0.S1'.S2'.S3' Y9=A.S0.S1'.S2'.S3 Y10=A.S0.S1'.S2.S3' Y11=A.S0.S1'.S2.S3 Y12=A.S0.S1.S2'.S3' Y13=A.S0.S1.S2'.S3 Y14=A.S0.S1.S2.S3' Y15=A.S0.S1.S2'.S3
Logical expression

## Slide 50
De-Multiplexers
Logical circuit

## Slide 51
Flip-Flops
  SR (Set-Reset) Flip-Flop
  JK Flip-Flop
Data or Delay (D) Flip-Flop
Toggle (T) Flip-Flop
A flip-flop is a digital memory circuit that stores “one bit” of data.
Flip-flops are the primary blocks of the most sequential circuits. It is also called one-bit memory or binary. They acts as a memory elements in a sequential circuit.
SR
JK
D
T

## Slide 52
Registers
A register is a group of flip-flops with each flip-flop capable of storing one bit of information.
An n-bit register has a group of n flip-flops and is capable of storing any binary information of n bits.

## Slide 53
Registers
Data can be entered in serial or parallel form.
Serial form means one bit at a time,
while parallel form means all bits at a time.
The data can be entered and extracted in either serial or parallel form.
Classification of Registers
(Depending on the input and Output)
1) Serial Input Serial Output (SISO)
2) Serial Input Parallel Output (SIPO)
3) Parallel Input Serial Output (PISO)
4) Parallel Input Parallel Output (PIPO)
Classification of Registers
(Depending on the Application)
1) Shift Registers
2) Storage Register

## Slide 54
Registers
Serial Input, Serial Output Shift Register

## Slide 55
Registers
Data at “data in” will be present at the Stage A output after the first clock pulse.
After the second pulse, stage A data is transferred to stage B output, and “data in” is transferred to stage A output.
After the third clock, stage C is replaced by stage B; stage B is replaced by stage A; and stage A is replaced by “data in”.
After the fourth clock, the data originally present at “data in” is at stage D, “output”. The “first in” data is “first out” as it is shifted from “data in” to “data out”.

## Slide 56
Registers
Parallel-In, Serial-Out Shift Register
In stage D data will be present at the “data out” up until the first clock pulse.
Stage C data will be present at “data out” between the first clock and the second clock pulse.
Stage B data will be present between the second clock and the third clock.
Stage A data will be present between the third and the fourth clock.

## Slide 57
Registers
Serial-In, Parallel-Out Shift Register
After the first clock, the data at “data in” appears at QA.
After the second clock, the old QA data appears at QB; QA receives the next data from “data in”.
After the third clock, QB data is at QC.
After the fourth clock, QC data is at QD. This stage contains the data first present at “data in”. The shift register now contains four data bits.

## Slide 58
Registers
Parallel-In, Parallel-Out Shift Register
Applications: Storage Register or Buffer Register

## Slide 59
Bidirectional shift register with parallel load
Shift Registers

## Slide 60
A register that goes through a predetermined sequence of states upon the application of input pulses is called a counter.
The input pulses may be clock pulses or may originate from an external source. They may occur at uniform intervals of time or at random.
Counters are found in almost all equipment containing digital logic. They are used for counting the number of occurrences of an event and are useful for generating timing signals to control the sequence of operations in digital computers.
A counter circuit will usually employ flip-flops with complementing capabilities. Both Tand JK flip-flops have this property. Remember that a JK flip-flop is complemented if both its J and K inputs are 1 and the clock goes through a positive transition. The output of the flip-flop does not change if J = K = 0.
Binary Counters

## Slide 61
Binary Counters
Asynchronous Counters

## Slide 62
Binary Counters

## Slide 63
Binary Counters
Binary 4-bit Synchronous Up Counter

## Slide 64
Binary Counters
Binary 4-bit Synchronous Down Counter
In 4-bit Synchronous Down Counter by connecting the AND gates to the Q`output of the flip-flops. Here the counter starts with all of its outputs HIGH ( 1111 ) and it counts down on the application of each clock pulse to zero, ( 0000 ) before repeating again.

## Slide 65
Memory Unit
Word : The memory stores binary information in groups of bits called words.
Byte: A group of 8-bits is called a byte.
RAM: In random-access memory (RAM) the memory cells can be accessed for information
transfer from any desired random location. It is a temporary memory bank where
your computer stores data it needs to retrieve quickly.
Write and read operations
Block diagram of random access memory (RAM)
The two operations that a random-access memory can
perform are the write and read operations

## Slide 66
Memory Unit
Types of ROMs
ROM: Read-only memory (ROM) is a memory unit that performs the read operation only
PROM: PROM is a type of read-only memory that you can program once
EEPROM: (Electrically Erasable Programmable Read-Only Memory) is a use modifiable ROM.
It can be erased and reprogrammed (written to) repeatedly by applying an
electrical voltage.

## Slide 67: Data Representation
» Data Types
» Complements
» Fixed-Point Representation
» Conversion of Fractions
» Floating-Point Representation
» Other Binary Codes
» Error Detection Codes

## Slide 68
Number Systems
There are 4 types of number systems in digital electronics
          Decimal number system ( Base 10 )
          Binary number system ( Base 2 )
          Octal number system ( Base 8 )
          Hexa-decimal number system ( Base 16 )
Examples:
In hexadecimal number system, there are 16 symbols or number
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
List of first 20 numbers hexadecimal number system
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F, 10, 11, 12, 13
List of first 10 numbers octal number system
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11
Review of Number systems and Codes

## Slide 69
Number Systems
Base Conversions
Convert (48)10 = ( )2
Convert (72)10 = ( )2
Convert (525)10 = ( )2
Convert (482)10 = ( )2
Convert (661)10 = ( )2
Convert (48.225)10 = ( )2
Convert (83.525)10 = ( )2
Decimal to Binary
Convert (48)10 = ( )8
Convert (125)10 = ( )8
Convert (93)10 = ( )8
Convert (154.125)10 = ( )8
Convert (23.225)10 = ( )8
Decimal to Octal
Convert (31)10 = ( )16
Convert (49)10 = ( )16
Convert (61)10 = ( )16
Convert (70.250)10 = ( )16
Convert (92.150)10 = ( )16
Decimal to Hexa

## Slide 70
Number Systems
Base Conversions
Convert (1100001)2 = ( )10
Convert (100001010)2 = ( )10
Binary to Decimal
Convert (31)8 = ( )10
Convert (125)8 = ( )10
Convert (731)8 = ( )10
Octal to Decimal
Convert (1F)16 = ( )10
Convert (3E)16 = ( )10
Convert (4A)16 = ( )10
Convert (5C.266)16 = ( )10
Convert (92.150)10 = ( )16
Hexa to Decimal

## Slide 71
Number Systems
Base Conversions
Convert (1100001)2 = ( )8
Convert (100001010)2 = ( )8
Binary to Octal
Convert (100001)2 = ( )16
Convert (10000110)2 = ( )16
Binary to Hexa
Octal to Binary
Hexa to Binary

## Slide 72
Binary Addition
8 + 7
7 + 7
15 + 15
5 + 5

## Slide 73
Binary Subtraction
8 - 7
8 - 15
73 - 23
-73 - 23

## Slide 74
Perform the arithmetic operation (+77) + (-23) and (-77) - (-23) in binary using signed 2’s complement representation for negative numbers.
Problems

## Slide 75
Fixed point Representation
0.95 + (-0.555)
0.88 – 0.15
0.75 + (-0.65)
Problems

## Slide 76
Convert the (-5.96)10 to binary number using 8-bit binary representation with 4-digit integers and 4-digit fractional parts.
Problems

## Slide 77
Floating point Representation
(7924.622)10
Problems
Double Perception Method
(1.N)2E-1023
(1.N)2E-127
Single Perception Method

## Slide 81
Other Binary Codes
Grey Code